## Slide 1: The Structural Simulation Toolkit (SST)
The SST Team
SAND2020-12392 TR

## Slide 2: Agenda
1000-1005 LPS/P38 Introduction
1005-1100 SST Overview & Configuration
1100-1200 Developing with SST
1200-1215 Break
1215-1245 P38 Scatter/Gather Experiments
1245-1330 Memory hierarchy (Gwen/Scott?)
1330-1345 Break
1345-1415 Broader SST Community (LLNL, GPGPUSim, GeM5)
1415-1445 Open Discussion

## Slide 3: Agenda
1000-1005 LPS/P38 Introduction
1005-1100 SST Overview & Configuration
  SST Overview
  Configuring & Use
  SST Element Libraries
1100-1200 Developing with SST
1200-1215 Break
1215-1245 P38 Scatter/Gather Experiments
1245-1330 Memory hierarchy (Gwen/Scott?)
1330-1345 Break
1345-1415 Broader SST Community (LLNL, GPGPUSim, GeM5)
1415-1445 Open Discussion

## Slide 4: Instructors
Arun Rodrigues afrodri@sandia.gov
Gwen Voskuilen grvosku@sandia.gov
Scott Hemmert kshemme@sandia.gov

## Slide 5: References
Websites
  http://www.sst-simulator.org/
  https://github.com/sstsimulator
Configuration File Format:
  http://sst-simulator.org/SSTPages/SSTUserPythonFileFormat/
Doxygen Documentation:
  http://sst-simulator.org/SSTDoxygen/9.0.0_docs/html/
Developer FAQ:
  http://sst-simulator.org/SSTPages/SSTTopDocDeveloperInfo/
Building SST
  http://sst-simulator.org/SSTPages/SSTBuildAndInstall9dot0dot0SeriesQuickStart/
  http://sst-simulator.org/SSTPages/SSTBuildAndInstall9dot0dot0SeriesDetailedBuildInstructions/

## Slide 6: Simulation Intersections
Project 38 Goal: More collaborative engagement than previous ‘special projects’
SST
  Modular
  Simple interfaces
  Designed for working w/ industry or closed projects
  Has extensive cache, coherency, main memory models
Vehicle for collaboration
  Have existing SST models
  Could help integrate vendor models

## Slide 7: Why SST? Another simulator?!
Problem: Simulation is slow
  Tradeoff between accuracy and time to simulate
  Many simulators are serial, with limited ability to model large, complex systems
Problem: Lack of simulator flexibility
  Want to combine single-purpose simulations to model system behavior
  Tightly-coupled simulators: faster but difficult to modify (e.g., change network topology…)
  Adding new functionality often requires significant effort
The Structural Simulation Toolkit: A parallel, discrete-event simulation framework for scalability and flexibility

## Slide 8: The Structural Simulation Toolkit
Goals
Create a standard architectural simulation framework for HPC*
Ability to evaluate future systems on DOE/DOD workloads
Use supercomputers to design supercomputers
Status
Parallel framework (SST Core)
Integrated libraries of components (Elements)
Current Release (9.0)
  https://sst-simulator.org
  https://github/sstsimulator
Technical Approach
Parallel Discrete Event core
  With conservative optimization over MPI/Threads
Interoperability
  Node and system-scale models
Multi-scale
  Detailed (~cycle) and simple models that interoperate
Open
    Open Core, non-viral, modular
Consortium
“Best of Breed” simulation suite
Combine Lab, Academic & Industry

## Slide 9: SST Architecture
SST Core framework
  The backbone of simulation
  Provides utilities and interfaces for simulation components (models)
    Clocks, event exchange, statistics and parameter management, parallelism support, etc.
SST Element libraries
  Libraries of components that perform the actual simulation
  Elements include processors, memory, network, etc.
    Includes many existing simulators: DRAMSim2, Spike, HMCSim, Ramulator, etc.
Integration Services
MPI and C++ Threads
Component
Component
Component
Component
SST Core

## Slide 10: SST: A Framework for Parallel Simulation
High-Level View

## Slide 11: Key objects
SST::Component
  Simulation model
SST::Link
  Communication path between two components
  Poll or interrupt with EventHandler
SST::Event
  A discrete event
SST::Clock::Handler
  Function to handle a clock tick
SST::SubComponent
  Add functionality to Components
SST::Link
SST::Component
CPU
EventHandler
SST::Component
Cache
EventHandler
SST::Event
Load
SST::Event
Data

## Slide 12: Component
Performs the actual simulation
Sends events over links to communicate with other components
  Components define ports, links connect ports between components
  Polled: Register a clock handler to poll the link
  Interrupt: Register an event handler to be called when an event arrives
Can load SubComponents and Modules for additional functionality
  Useful for parts of a component that should be swappable between simulations
    Ex: scheduling algorithms, address mapping schemes, cache prefetchers
  Useful for exposing interfaces to other components
    Ex: network provides a subcomponent that can be loaded to handle traffic into/out of network
DIMM
ROUTER
NETWORK
TRAFFIC GENERATOR
CPU
$$
CACHE

## Slide 13: Link
Connects two components
  Connect a specific named “Port” on component A to a “Port” on component B
The ONLY mechanism by which components communicate
  Necessary for parallel simulation
Has a minimum, non-zero latency for communication
  Except self-links
  Except during init/complete phases (untimed)
Transparently handles any MPI / threaded communication
Component A
Component B
Port X
Port Y
Link 1

## Slide 14: Event
Unit of communication between two components
  Packet format is up to the communicating components
Some standardized interfaces
  Facilitates “mix and match” capability
  sst-core/interfaces/
  Memory (simpleMem)
    Defines commands & event format for communication with caches & memory
  Network (simpleNetwork)
    Defines a packet format for events sent through a network component

## Slide 15: SST Building Blocks
SST simulations are comprised of components connected by links
Components communicate by sending events over the links
  Components define ports which are valid connection points for a link
Components can use subComponents and modules for extra functionality
SST Component
Core
SST Component
Cache
SST Component
Core
SST Component
Cache
SST Component
NoC Router
SST Component
NoC Router
SST Link
Latency: 1ns
SST Link
Latency: 2ns
SST Link
Latency: 2ns
SST Link
Latency: 1ns
SST Link
Latency: 4ns
SubComponent
Prefetcher

## Slide 16: Simulating with SST

## Slide 17: Getting and Installing SST
http://www.sst-simulator.org
  Current release source download
  Detailed build instructions including dependencies for Linux & Mac
  Archived tutorial materials
https://github.com/sstsimulator
  Source code checkout
  Master branch – has passed testing
  Devel branch – has passed basic testing

## Slide 18: SST Code Structure
SST Core and SST Elements are compiled separately
  Element libraries register with the core
  External elements (not part of SST Elements) can also be registered with the core
    Example at github.com/sstsimulator/sst-external-element
  Core maintains a database of registered libraries
    Can query database with sst-info utility
Source code for core:
  sst-core/src/sst/core/
Source code for elements
  sst-elements/src /sst/elements/
  Most elements have a tests/ directory
    Often a good starting point for example configurations
Integration Services
MPI and C++ Threads
Component
Component
Component
Component
SST Core

## Slide 19: Simulation Configuration
To define simulations, users create a python configuration file which:
  Defines the components and subcomponents to use
  Specifies the connectivity between components
SST then:
  Loads the file and converts it to a graph
  Partitions the graph for parallel simulation
  Instantiates the components
  Runs the simulation!

## Slide 20: Simulation Lifecycle
Birth
  Create graph of components using Python configuration file
  Partition graph and assign components to MPI ranks
  Instantiate components
  Connect components via links
  Initialize components using their init() functions, multi-phase initialization
  Setup components using their setup() functions
Life
  Send events
  Manage clock and event handlers
Death
  Complete simulation using components’ complete() functions, multi-phase quiesce
  Finalize components using their finish() functions
  Output statistics
  Cleanup simulation, delete components

## Slide 21: Configuration File: Global SST parameters
Set any global simulation parameters
  End simulation at 100ms if it hasn’t ended already
Other options
  Most are also available as command line arguments to SST
Option | Definition
debug-file | File to print debug output to
heartbeat-period | If set, SST will print a heartbeat message at the specified period
timebase | Units of simulation. Default is picoseconds which enables 2/3 of a year.
partitioner | Partitioner to use for parallel execution
output-partition | File to print partition to
SST Python API
User-defined string
SST argument
sst.setProgramOption(“stopAtCycle”, “100ms”)

## Slide 22: SST Partitioners
General Partitioners
  linear: Partitions components by dividing Component ID space into roughly equal portions. Components with sequential IDs will be placed close together.
  roundrobin: Partitions components using a simple round robin scheme based on ComponentID. Sequential IDs will be placed on different ranks.
  simple: Simple partitioning scheme which attempts to partition on high latency links while balancing number of components per rank.
  zoltan: zoltan parallel partitioner.
Special Partitioners
  single: Allocates all components to rank 0. Automatically selected for serial jobs.
  self: Used when partitioning is already specified in the configuration file (see next slide).

## Slide 23: Self Partitioning
Partitioning can be specified in the python input file
    Use setRank(mpi_rank, thread) on a component
      User must set rank/thread pairs for all components in system, partial partitions not supported
      Example:
      or
Must set the partitioner to be ”self”
  Can be done on command-line: --partitioner=self
  Can be done in python file: sst.setProgramOption(”partitioner", ”self")
comp = sst.Component(“lib.element”)
comp.setRank(5, 4) # put this on rank 5, thread 4
comp = sst.findComponentByName(“my_comp_name”)
comp.setRank(5, 4) # put this on rank 5, thread 4

## Slide 24: Configuration File: Declare components and links
Components: sst.Component(“name”, “type”)
Links: sst.Link(“name”)
core = sst.Component(“core”, “miranda.BaseCPU”)
cache = sst.Component(“L1”, “memHierarchy.Cache”)
mctrl = sst.Component(“memctrl”, “memHierarchy.MemController”)
link0 = sst.Link(“core_to_cache”)
link1 = sst.Link(”cache_to_memory”)
Component name
Component library.type
Core
Cache
MemCtrl
Link name
SST Python API
User-defined string
SST argument
Gen
Mem

## Slide 25: Configuration File: Configure the components
Parameters: addParams({ “parameter” : “value”, … })
SubComponents: setSubComponent(“slotname”, “type”)
  Recall: SubComponent is a swappable piece of functionality
core.addParams({ “clock” : “2.4GHz” })
Core
Cache
MemCtrl
gen = core.setSubComponent(“generator”, “miranda.STREAMBenchGenerator”)
memory = mctrl.setSubComponent(“backend”, “memHierarchy.simpleMem”)
SST Python API
User-defined string
SST argument
How do I know what the options are? Or even what elements I can pick from?
Gen
Mem

## Slide 26: SSTInfo: Getting component info
sst-info: utility to query element libraries
$ sst-info miranda.BaseCPU
PROCESSED 1 .so (SST ELEMENT) FILES FOUND IN DIRECTORY(s) /home/sst/build/sst-elements/lib/…
Filtering output on Element = “miranda.BaseCPU”
================================================================================
ELEMENT 0 = miranda ()
Num Components = 1
Component 0: BaseCPU
CATEGORY: PROCESSOR COMPONENT
NUM STATISTICS = 17
…
NUM PORTS = 2
PORT 0 = cache_link (Link to Memory Controller)
…
NUM SUBCOMPONENT SLOTS = 2
SUB COMPONENT SLOT 0 = generator (What address generator to load) [SST::Miranda::RequestGenerator]
…
NUM PARAMETERS = 12
PARAMETER 0 = clock (Clock for the base CPU) [2GHz]
…
Optionally filter for a specific library and/or component
Parameter
Definition
“REQUIRED” or default value
Port name
Definition
Slot name
Definition
SubComponent API

## Slide 27: Configuration File: Connecting the components
Declared links and components a couple slides ago…
Connect components: connect(endpoint1, endpoint2)
  Where endpoint is: (component, port, latency)
link0 = sst.Link(“core_to_cache”)
link1 = sst.Link(“cache_to_memory”)
link0.connect(
(core, “cache_link”, “100ps”),
(cache, “high_network_0”, “100ps”) )
link1.connect(
(cache, “low_network_0”, “100ps”),
(mctrl, “direct_link”, “100ps”) )
Endpoint 1
Endpoint 2
Core
Cache
MemCtrl
core = …
cache = …
mctrl = …
Gen
Mem

## Slide 28: Running a simulation
Launch (serial) simulation
Launch (threaded) simulation
Output
$ sst demo0.py
<Simulation Specific Output>
Simulation is complete, simulated time: 6.66491 us
$ sst –n <#threads> demo0.py

## Slide 29: SST Elements: A Quick Tour

## Slide 30: SST 9.0 Elements
Processors
  Ariel – PIN-based
  Juno – simple ISA processor
  Miranda – pattern generator
  Prospero – trace execution
  GeNSA – Spiking temporal processing unit
  Spike – RISC-V model by TCL
Memory Subsystem
  cacheTracer – cache tracing
  Cassini – cache prefetchers
  CramSim – DDR, HBM
  MemHierarchy – caches, directory, memory
  Messier - NVM
  Samba – TLB
  VaultSimC – vaulted stacked memory
Network drivers
  Ember – communication patterns
  Firefly – communication protocols
  Hermes – MPI-like driver interface
  Zodiac – trace based driver
  Thornhill – memory models for Ember sims
Networks/NoCs
  Merlin – flexible network modeling
  Kingsley – mesh NoC
  Shogun – crossbar NoC
Others
  sst-macro – network drivers/network
  scheduler – job scheduling
  simpleSimulation – “car wash” example
  simpleElementExample – many examples
  sst-external-element – example element

## Slide 31: Ariel: PIN-based processor
Lightweight processor core model
Uses Intel’s PIN tools and XED decoders to analyze binaries
  Runs x86, x86-64, SSE/AVX, etc. binaries
  Supports fixed thread count parallelism (OpenMP, Qthreads, etc.)
Passes instructions to virtual core in SST
Processor
Memory
Other
Network/NoC
Network driver
GPGPU-Sim Integration
Used in P38 Experiments

## Slide 32: Prospero: Trace-based processor
Trace-based processor model
  Like Ariel, memory instruction oriented
    Reads memory ops from a file and passes to the simulated memory system
  “Single core” but can use multiple trace files to emulate threaded or MPI applications
  Supports arbitrary length reads to account for variable vector widths
  Performs “first touch” virtual to physical mapping
Comes with Prospero Trace Tool to generate traces
  Or can generate your own and translate to Prospero’s format
Processor
Memory
Other
Network/NoC
Network driver

## Slide 33: Miranda: Pattern-based processor
Extremely light-weight processor model
  Generates memory address patterns
  Supports request dependencies
Library patterns
  Strided accesses (single stream)
    Forward and reverse strides
  Random accesses
  GUPS
  STREAM benchmark
    In-order & out-of-order CPU
  3D stencil
  Sparse matrix vector multiply (SpMV)
  Copy (~array copy)
  Stake interface to the Spike RiscV simulator
Processor
Memory
Other
Network/NoC
Network driver

## Slide 34: Vanadis processor pipeline model
Initial research concept for a ISA-agnostic RISC pipeline model for SST
  Provides MIPS32 ISA for simplicity and ease of development
  Individual cores can run as individual SST components but can link together for single memory / address space (promotes parallelism)
  Provides operating system emulation mode (does not need to boot a kernel etc)
  Decoders are full SST sub-components so can be extended and swapped out
    On a per-hardware thread or per-core basis
Pipeline is out-of-order and parameterized to permit hardware exploration
  Execute-at-execute pipeline model
  External memory (required for parallelism)
  Functional units are fully extensible/swappable and individually parameterizable
  Ability to add (custom) instructions into the pipeline (exploring put/get, thread mgmnt)
Still in development but initial simple runs of binaries complete successfully
  Intended to be an initial “alpha” component release with SST 11.0
Work In Progress
Processor
Memory
Other
Network/NoC
Network driver

## Slide 35: Vanadis Concept designs
Vanadis Core
@ 2.5GHz
L1D
L1I
L2 (2MB)
NoC
Vanadis Core
@ 1.0GHz
L1D
L1I
L2 (128kB)
Mem Ctrl
Vanadis OS Handler
Vanadis Core
@ 1.0GHz
L1D
L1I
L2 (128kB)
…
Many small cores
Big Core
HBM Model (CRAMSim?)
Example mix-core node design
Vanadis Core
@ 2.5GHz
L1D
L1I
L2 (2MB)
NoC
Mem Ctrl
Vanadis OS Handler
Big Core
HBM Model (CRAMSim?)
Example accelerated node design
GPGPU
@ 1.0GHz
L2 Shim
…
Vanadis Core
@ 2.5GHz
L1D
L1I
L2 (2MB)
NoC
Mem Ctrl
Vanadis OS Handler
Big Core
HBM Model (CRAMSim?)
Example processing in memory node design
Vanadis Core
@ 300MHz
Vanadis Core
@ 300MHz
Vanadis Core
@ 2.5GHz
L1D
L1I
L2 (2MB)
Big Core
Flexibility and parameterization of Vanadis allows it to be used in many different design scenarios
Integration with SST allows significant degree of flexibility
Potential for different cores to have different ISAs (e.g. PIM use case)
…

## Slide 36: MemHierarchy: Memory system
Collection of interoperable memory system elements
  Caches
  Directories
  Memory controllers
    Interfaces to memory models (DDR, HBM, HMC, NVM, etc.)
  Scratchpads
  NoC (network-on-chip) interfaces
  Buses
Components are cycle-accurate/cycle-level
Capable of modeling modern cache and memory subsystems
Processor
Memory
Other
Network/NoC
Network driver
Deep Dive This Afternoon
Used in P38 Experiments

## Slide 37: Merlin / Kingsley: Network simulator
Low-level networking components that can be used to simulate high-speed networks (machine level) or on-chip networks
Capabilities – Merlin
  High radix router model (hr_router)
  Topologies – mesh, n-dim tori, fat-tree, dragonfly
Capabilities – Kingsley
  NoC-focused
  Mesh topology, input only routing
Many ways to drive a network
  Simple traffic generation models
    Nearest neighbor, uniform, uniform w/ hotspot, normal, binomial
  MemHierarchy
  Lightweight network endpoint models (Ember – coming up next)
  Or, make your own
Processor
Memory
Network/NoC
Network driver
Other
Deep Dive This Afternoon
Used in P38 Experiments

## Slide 38: SST Overview
SST
  Parallel Conservative discrete event core
  Interoperability with many simulators
  Multi-scale operation
  Open: Non-viral license, open core
Easy Python-based configuration
Simple simulation lifecycle
Wide library of elements

## Slide 39: Questions?

## Slide 40: SST Element Libraries
Elements are libraries of related components
  Elements must be registered with the SST core
    Tells SST where to find this set of components
    Includes information on parameters and statistics for each component
SST provides a set of element libraries
  Processor, network, memory, etc.
  Tested for interoperability within and across libraries
  Many are compatible with external “components” such as Ramulator and Spike
    See www.sst-simulator.org for more information
You can also register your own elements

## Slide 41: Juno: Simple instruction processor
Executes a program written in simple “assembly”
  32-bit wide instructions with 8 bit op codes
  64-bit integer operations
    ADD, SUB, DIV, MUL,
    AND, OR, XOR, NOT
  Jump by register value (JGT-Zero, JLZ-Zero, J-Zero)
    Jump up to16 bits in either direction from current PC
  Up to 253 user registers
    r0 = PC
    r1 = data start register
Memory
Juno
Instruction Manager
Load/Store Unit
Register File
Processor
Memory
Other
Network/NoC
Network driver

## Slide 42: Ember: Overview
User
Binary
Ember Engine
Hermes API
Firefly
Merlin Network
Ember Motif
Message Passing Semantics
Collectives, Matching, etc.
Packetization and Byte Movement Engine
Generates packets and coordinates with network
Flit Level Movement, Routing, Delivery
Moves flits across network, timing, etc.
Event to Message Call, Motif Management
Handles the tracking of the motif
High Level Communication Pattern and Logic
Generates communication events
Processor
Memory
Network/NoC
Network driver
Other

## Slide 43: Ember: Network Traffic Generator
Light-weight endpoint for modeling network traffic
  Enables large-scale simulation of networks where detailed modeling of endpoints would be expensive
Packages patterns as motifs
  Can encode a high level of complexity in the patterns
  Generic method for users to extend SST with additional communication patterns
Intended to be a driver for the Hermes, Firefly, and Merlin communication modeling stack
  Uses Hermes message API to create communications
  Abstracted from low-level, allowing modular reuse of additional hardware models
Processor
Memory
Network/NoC
Network driver
Other

## Slide 44: Ember: Motifs
Motifs are lightweight patterns of communication
  Tend to have very small state
  Extracted from parent applications
  Models as an MPI program (serial flow of control)
    Many motifs acting in the simulation create the parallel behavior
Example motifs
  Halo exchanges (1, 2, and 3D)
  MPI collections – reductions, all-reduce, gather, barrier
  Communication sweeping (Sweep3D, LU, etc.)
Processor
Memory
Network/NoC
Network driver
Other

## Slide 45: Ember: Motifs (continued)
The EmberEngine creates and manages the motif
  Creates an event queue which the motif adds events to when probed
  The Engine executes the queued events in order, converting them to message semantic calls as needed
  When the queue is empty, the motif is probed again for events
Events correspond to a specific action
  E.g., send, recv, allreduce, compute-for-a-period, wait, etc.
Processor
Memory
Network/NoC
Network driver
Other

## Slide 46: Firefly: Network traffic
Purpose: Create network traffic, based on application communication patterns, at large scale
  Enables testing the impact of network topologies and technologies on application communication at very large scale
Scales to 1 million nodes
Supports multiple “cores” per Node
  Interaction between cores limited to message passing
Supports space sharing of the network
  Multiple “apps” running simultaneously
Processor
Memory
Network/NoC
Network driver
Other

## Slide 47: Firefly: Simulating large networks
A network node consists of
  Driver (the “application”)
  NIC
  Router
Nodes are connected together via routers to form a network
  Fat tree, torus, etc.
Firefly is the interface between the driver and the router
  Message passing library  Firefly Hades
  NIC  Firefly NIC
Ember
(driver)
Firefly Hades
Firefly NIC
Merlin Router
Processor
Memory
Network/NoC
Network driver
Other

## Slide 48: Scheduler: Job scheduling
Models HPC system-wide job scheduling
Three components
  Sched: schedules and allocates resources for a stream of jobs
  Node: runs scheduled jobs on their allocated resources
  FaultInjection: injects failures onto the resources
The scheduler can be a stand-alone element library
  The schedComponent and nodeComponent must be used together
  The faultInjectionComponent is optional
Can be used with Ember/Firefly/Merlin stack
  Examine topology aware scheduling and allocation
Processor
Memory
Network/NoC
Network driver
Other

## Slide 49: So many simulators, so little interoperability
Already a rich selection of open-source simulators
But not a solid ecosystem for modeling systems
  Tightly-entangled components make modifications complex
    E.g., assumptions about caching or address mapping pervasive
  Most simulator integrations are ad-hoc, not lasting
  Significant performance problems with tying many simulators together
Wants:
  Enable “mix-and-match” of existing models to create custom systems
  Encourage disentangled models with clean interfaces for swapping functionality
    Bricks not buildings
  Low effort, high performance parallel simulation
  Continuous path from low-fidelity/fast modeling to high-fidelity/slow models

## Slide 50: SubComponents and Modules
Add additional functionality to a Component
  SubComponent (SC): shares common base class with Component
  Module (M): self-contained functionality (no access to Component class functionality
Provide modularity
  Generic interface which can be used by multiple SC/M
  Components load SC/M at runtime
Tightly-coupled with a component
  Components call SC/M as a C++ class instance
  Do not need to communicate via links
  SC/M cannot exist by themselves
Example
  Miranda core loads a pattern generator subcomponent to generate a sequence of memory ops
Component: Core
SubComponent: Stream Gen
Component: Core
SubComponent: SpMV Gen
Component: Core
SubComponent: Random Gen
or
or
Notes: Finish: define subcomponent & module!

## Slide 51: Component/Link Interface
Components use these calls to manage links and events
SST::Component::configureLink()
  Registers a link and (optionally) a handler
SST::Link::recv()
  Pull an event from a link
SST::Link::send()
  Push an event down a link
SST::Component::registerClock()
  Register a clock frequency and a handler to be called on each clock tick

## Slide 52: Simulating with SST
We’ll walk through how to configure a simulation and then run it
  Available at: https://github.com/sstsimulator/sst-tutorials/tree/master/pact2019/demos
  ( github  sstsimulator  sst-tutorials  pact2019 )
Element libraries in our example simulation
  Miranda - Simple core model that runs generated instruction streams
    Generators produce memory access patterns (SubComponents)
  memHierarchy – Various cache/memory system related subcomponents and modules
    Cache (Component) with coherence protocol SubComponent
    Memory Controller (Component) that loads a memory timing model (SubComponent)
Core
L1 Cache
MemCtrl
2KB, 4-way set associative
2.4GHz, 2 cycle access
64B cache lines
LRU replacement MESI coherence protocol
2.4GHz, issue 2 accesses/cycle
Stream triad generator
Three 1K element arrays A,B,C
Compute C[i] = A[i] + 2*B[i]
 2K reads & 1K writes
50ns constant access latency
1GB capacity
Gen
Mem

## Slide 53: SST in Parallel
SST was designed from the ground up to enable scalable, parallel simulations
Components distributed among MPI ranks
  And/or threads
Links allow parallelism
  Hence, components should communicate via links only
  Transparently handle any MPI/thread communication
  Specified link-latency determines synchronization rate
MPI Rank 0
MPI Rank 0
MPI Rank 1
MPI Rank 2
MPI Rank 3
Comp0
Comp2
Comp4
Comp6
Comp1
Comp3
Comp5
Comp7
Comp0
Comp2
Comp4
Comp6
Comp1
Comp3
Comp5
Comp7
Same configuration file
Notes: Links handle serialization

## Slide 54: Enabling statistics
Most Components and SubComponents define statistics
Enable statistics in the configuration file
  enableAllStatisticsForAllComponents()
  enableAllStatisticsForComponentType(type)
  enableAllStatisticsForComponentName(name)
  setStatisticLoadLevel(level)
Configure output
  setStatisticOutput(“sst.output_type”)
  setStatisticOutputOptions({“option” : “value”, })
  enableStatisticForComponentName(name, stat)
  enableStatisticForComponentType(type, stat)
$ sst-info memHierarchy.Cache
…
NUM STATISTICS = 51
STATISTIC 0 = CacheHits [Total number of cache hits] (count) Enable Level = 1
STATISTIC 1 = latency_GetS_hit [Latency for read hits] (cycles) Enable level = 1

## Slide 55: Running with statistics enabled
Let’s enable statistics for all components
  Caches have A LOT of statistics so send the output to a CSV file
  Other options: sst.statoutputX where X=
    console
    json
sst.setStatisticOutput(“sst.statoutputcsv”)
sst.setStatisticOutputOptions({ “filepath” : “stats.csv” })
sst.setStatisticLoadLevel(5)
sst.enableAllStatisticsForAllComponents()
    txt
    hdf5

## Slide 56: Running SST
Usage: sst [options] configFile.py
Common options:
-v ¦ --verbose | Print information about core runtime
--debug-file <filename> | Send debugging output to specified file (default: sst_output)
--partitioner <zoltan ¦ self ¦ simple ¦ rrobin ¦ linear ¦ lib.partitioner.name> | Specify the partitioning mechanism for parallel runs
-n ¦ --num_threads <num> | Specify number of threads per rank
--model-options “<args>” | Command line arguments to send to the Python configuration file
--output-partition <filename> | Write partitioning information to <filename>
--output-dot <filename> --output-xml <filename> --output-json <filename> | Output the configuration graph in various formats to <filename>
Notes: Is this still up to date?

## Slide 57: SST in a Nutshell
Parallel Discrete-Event Simulator Framework
  Flexible framework enables multitude of custom “simulators”
  Demonstrated scaling to over 512 processors
Comes with many built-in simulation models
  Processors, memory, network
  “Mix & Match”
Open API
  Easily extensible with new models
  Modular framework
  Open-source core
Time-scale independent core
  Handles Micro-, Meso-, Macro-scale simulations
C++, Python
CPU
Network
Memory
CPU

## Slide 58: SST in parallel
SST was designed from the ground up to enable scalable, parallel simulations
Components distributed among MPI ranks/threads
  Link latency controls synchronization rate
MPI Rank 0
MPI Rank 0
MPI Rank 1
MPI Rank 2
MPI Rank 3
Comp0
Comp2
Comp4
Comp6
Comp1
Comp3
Comp5
Comp7
Comp0
Comp2
Comp4
Comp6
Comp1
Comp3
Comp5
Comp7
Same configuration file
# Two ranks
$ mpirun –np 2 sst demo1.py
# Two threads
$ sst –n 2 demo1.py
# Two ranks with two threads each
# This will give a warning since we only
# have 3 components across 4 ranks/threads
$ mpirun –np 2 sst –n 2 demo1.py
Notes: Links handle serialization

## Slide 59: Prospero: The Tradeoff
Pros
  Faster than Ariel*
    Provided you can get a trace
Cons
  Traces can be very large
    Requires good I/O system to store and read the trace
  Traces are less flexible than actual execution
    Capture a single execution stream using a single application input
Processor
Memory
Other
Network/NoC
Network driver

## Slide 60: Miranda: The tradeoffs
Pros
  Very lightweight – no binary, no trace
  Good for applications whose address patterns are predictable
    e.g., not much pointer-chasing
  Models instruction dependences
Cons
  Need a generator for the memory pattern of interest
    Requires a good understanding of the pattern
Processor
Memory
Other
Network/NoC
Network driver

## Slide 61: MemHierarchy: Cache modeling
Highly configurable
  Arbitrary hierarchy depth, flexible topologies
  Cache inclusivity, coherence, private/shared, etc. configurable
  Single- and multi-socket configurations
  Prefetch via Cassini element library
Data movement
  Components support direct, bus, and on-chip network (NoC) communication
Event types: read/write, atomics, LLSC, noncacheable, custom memory, etc.
Processor
Memory
Other
Network/NoC
Network driver

## Slide 62: MemHierarchy: Memory modeling
Interface to memory is the MemController
MemControllers implement backends
  Timing model for memory controller with a link to memory
  Timing model for memory controller and memory
  Interface to another component(s) that does the memory controller/memory timing
    In this case just translates request formats
  Wrapper for an external/non-native-SST component
    Ramulator, DRAMSim2, etc.
Support custom memory instructions
  Including ability to do cache shootdowns for coherence maintenance
Processor
Memory
Other
Network/NoC
Network driver

## Slide 63: MemHierarchy: Memory modeling
Memory controller
  Manages data values if needed (backing store)
  Facilitates custom memory commands
    Including cache shootdowns for coherence maintenance
  Passes events to memory backend subcomponent
Backend: the “real” memory controller and/or memory
  Implementations
    Memory controller and model itself
    Memory controller with interface to a memory component
    Interface to another memory controller/memory component
    Wrapper to an external simulator
Memory Controller
Backend
Backing store
Custom command handler
To memory component (optional)
Processor
Memory
Other
Network/NoC
Network driver

## Slide 64: MemHierarchy: SST 9.0 backends
Memory (external)
  CramSim (DDR, HBM)
  DRAMSim2 (DDR)
    PagedMulti – 2-level memory variant
  FlashDIMMSim (FLASH)
  HMCSim/GoblinHMC (HMC)
  HBMDRAMSim2 (HBM)
    HBMPagedMulti – 2-level memory variant
  Messier (NVRAM)
  Ramulator (DDR, HBM, HMC)
  SimpleDRAM (DDR)
  SimpleMem (constant latency)
  TimingDRAM (DDR)
  VaultSimC (HMC-like)
Plus a few that can be used with other backends to reorder requests, add latency, etc.
Processor
Memory
Network/NoC
Network driver
Other

## Slide 65: Merlin: Organization
PC
PC
PC
PC
PC
PC
PC
PC
Topology
XBAR
Router
PC = PortControl
LC
LC = LinkControl
TrafficGen
TestNIC
User Logic
NIC
Processor
Memory
Network/NoC
Network driver
Other

## Slide 66: Kingsley: Mesh simulator
Network-on-chip model; mesh configuration
Similar to Merlin but:
  No input queuing at routers
  Mesh topology only
  Not all ports need to be populated
  Possible to instantiate multiple unconnected networks
    Multiple physical networks for coherence (e.g., request/response/ack/forward)
    Kingsley NoC + Merlin/Kingsley system network
Processor
Memory
Network/NoC
Network driver
Other
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
NIC
Interconnect