## Slide 1: P38 Scatter Gather Experiments
The SST Team
SAND2020-12393 TR

## Slide 2: Agenda
1000-1005 LPS/P38 Introduction
1005-1100 SST Overview & Configuration
1100-1200 Developing with SST
1200-1215 Break
1215-1245 P38 Scatter/Gather Experiments
1245-1330 Memory hierarchy (Gwen/Scott?)
1330-1345 Break
1345-1415 Broader SST Community (LLNL, GPGPUSim, GeM5)
1415-1445 Open Discussion

## Slide 3: P38 Background
Initial Discussions (Sept 2017)
  Brainstorm Architecture Ideas (e.g. “S/G”)
Summer 2018
  Explore small set of architectures
  Define applications scope
Late 2018-2019
  Application Analysis
  Refine Architectural ideas
  Exploring software
Exploration Goals
  Is there a “win” here?
  Upside potential
Simulation Goals
  Evaluate Implementation options
  Foundation for future collaboration
Notes: QUICK
Cultural & organizational constraint space
As well as how we organize research efforts

## Slide 4: Application Analysis Infrastructure

## Slide 5: Simple Analysis: Instruction Mix
Dynamic Instruction Mix
  ~40-50% Memory
  ~20-40% Integer
  ~15-40% Other (Branch, FP, etc…)
Most Integer instructions calculating memory addresses

## Slide 6: Application Analysis Goals
Find Applications of interest
  Potential “wins”, but still realistic
Understand what access patterns look like
Develop techniques to identify likely offload / scatter-gather sections

## Slide 7: Key Components
Ariel Processor Model
MemHierarchy
  Caches
  Dir. Controller
  Mem Controller
Merlin Network Model

## Slide 8: Key Components
Ariel Processor Model
MemHierarchy
  Cache
  Dir. Controller
  Mem Controller
Merlin Network Model

## Slide 9: Ariel: PIN-based processor
Lightweight processor core model
Uses Intel’s PIN (dynamic binary instrumentation)
Passes instructions to virtual core in SST via shared memory
Ariel’s virtual cores
  Memory instruction oriented: execute memory instructions; other ins. single cycle
  Does not maintain dependence order or register locations
Key parameters
  Ops issued/cycle
  Load/store queue size
Processor
Memory
Other
Network/NoC
Network driver

## Slide 10: Ariel: The Tradeoff
Pros:
  Faster than more complex/pipeline models
  Software: easy to target, malleable
  Reasonable approximation for studies on memory system performance
    Especially for heavily memory-bound applications
  Reasonable model of thread interactions
Cons
  Non-deterministic results
    Interactions between pintool, threads, etc.
    Variation is low (O(1%))
  Not compatible with non-x86 binaries
  Reliant on Pin
  Less accurate for heavily compute-bound
Processor
Memory
Other
Network/NoC
Network driver

## Slide 11: MemHierarchy: Memory system
Collection of interoperable memory system elements ($s, directories, scratchpad, etc…)
  Components are cycle-accurate/cycle-level
Cache Model
  Arbitrary hierarchy depth, flexible topologies
  Cache inclusivity, coherence, private/shared, etc. configurable
  Single- and multi-socket configurations
Memory Controller backends:
  Simple Timing Model
  Basic DRAM timing (sense amp delay)
  Wrappers for an external/non-native-SST simulators
    Ramulator, DRAMSim2, etc.
Processor
Memory
Other
Network/NoC
Network driver
More This Afternoon

## Slide 12: Merlin Network simulator
Low-level networking components that can be used to simulate high-speed networks (machine level) or on-chip networks
Capabilities – Merlin
  High radix router model (hr_router)
  Topology: Crossbar
Network
  4 processor clusters
    4 cores/cluster
    4 L1s 4 (optional) scratchpads
    1 L2 $
  Memory Controller (DRAMSim2)
Processor
Memory
Network/NoC
Network driver
Other
More This Afternoon

## Slide 13: Analysis Infrastructure
CacheLineTrack
  Subcomponent
  “Cache Listener”
  Built on interface for prefetchers: notified of reads, writes, evictions
  Gathers post-cache histograms, cache use stats, etc…
  accPat “Access Pattern Tracker”
    Added to a memory controller model
    Tracks access patterns by “page”
  Allows….
…/elements/cassini/cacheLineTrack.*
…/elements/memHierarchy/membackend/pagedMultiBackend.*

## Slide 14: Words Touched Before $ Evict
a
🙂
🙂
Better understanding of where caches aren’t working
Notes: Smily in the sense that there is room for the improvement – it could be a frown in the sense that we are very wasteful

## Slide 15: Reads Before Evict
L1s: Lots of variation
  6 (XSBench) to 68 (hpgmg) reads before eviction
  Most $lines <16
L2s
  Much less (2-3) reads before evict
Writes broadly similar
Useful for identifying scratchpad candidates

## Slide 16: Threads/Page Access
a
😐
🙂
🙁
☹️
Will thread sharing complicate implementation?

## Slide 17: Usage Histograms
In most applications, small number of pages account for disproportionate number of accesses
Small cache can capture a lot
Diminishing returns as $ gets larger
Useful for Scratchpad sizing

## Slide 18: Access Pattern Detection
First quick cut of access pattern detection
Examines post-cache misses
Determines simple pattern (5 classes)
Cluster Centers
How complex are access patterns?

## Slide 19: MiniMD: Memory Hotspots
3 sites in one file
Good capture
May require atomics (FP+)
miniMD/kokkos/force_lj.cpp:
void ForceLJ::operator():
const MMD_float xtmp = x(i,0);
const MMD_float ytmp = x(i,1);
const MMD_float ztmp = x(i,2);
for(int k = 0; k < numneighs; k++) {
const MMD_int j = neighbors(i,k);
const MMD_float delx = xtmp - x(j,0);
const MMD_float dely = ytmp - x(j,1);
const MMD_float delz = ztmp - x(j,2);
const int type_j = type[j];
}
f_a(i,0) += fix;
f_a(i,1) += fiy;
f_a(i,2) += fiz;
Which regions should be targeted?

## Slide 20: Scatter/Gather Evaluation

## Slide 21: S/G Evaluation Goals
Identify regions of selected applications that may be amenable to near-memory “scatter-gather”
Estimate total application performance improvement

## Slide 22: Evaluation Infrastructure
Added Scratchpad
Added Prefetch logic to Ariel
  Emulates near-memory accesses
  S/G mem ops queue’d up (Prefetch Queue)
  Consolidates scatter-gather accesses
  Adds latency, throttles issue width
  Sends to memory
  Loads to $ or scratchpad

## Slide 23: Evaluation Infrastructure: Application
Modified applications based on analysis
“Tag” S/G sections
Send tagged/ annotated stream back to Ariel
Track & gather statistics

## Slide 24: Evaluation Infrastructure: Application Interface
Normal Ariel just passes reads/writes and other instructions back to Ariel CPU
Modifications for P38
  Add “buoy” functions which PIN replaces with markers
  Toggling to indicate non-memory instructions (i.e. would be offloaded)
  Prefetch loads (coalesced, sent directly to memory)
    Optionally, return to scratchpad
https://github.com/afrodri/sst-elements/tree/afrodri/sgEst
…/elements/ariel/frontend/simple/ fesimple.cc
…/elements/ariel/arielcore.cc

## Slide 25: Initial Applications: Kripke, hpgmg, XSBench
Applications modified
Difficult! High bar:
  Kripke: 98% L1 hit, high L2, multiple “hot” s/g regions, ~70% accesses in s/g, thread local
  hpgmg: 98-99% L1 hit 😰
  XSBench: upto 5% L1 miss, 30% s/g, complex s/g region
If we can show improvement here, we can probably improve many apps
😰
🙂
😰
😰

## Slide 26: Evaluation Infrastructure: Application Modifications
int scOff = 1;
for(int gz = 0;gz < num_locgz; ++ gz){
ariel_toggle();
ariel_pf(&psi_d[gz], scOff++);
ariel_pf(&phi_nm[gz], scOff++);
ariel_toggle();
}
for(int gz = 0;gz < num_locgz; ++ gz){
phi_nm[gz] += ell_nm_d * psi_d[gz];
}
Original Loop
“Prefetch Loop”
Toggle so non-memory not counted
Issue Prefetch (opt: To scratchpad)
PFs are coalesced to improve density
PFs to scratch have addresses remapped
Allows…

## Slide 27: Performance estimates
Effect 1: Reduce $ Misses
  Many L1 misses become hits
  13-40% IPC improvement
Effect 2: Integer offload
  17-44% IPC Improvement
Effect 3: Improved $ performance
  If covered cache accesses go to scatchpad, other accesses more efficient?
Chart: Estimated IPC Improvement from S/G
| hpgmg | Kripke | XSBench | miniMD
Reduced $ Misses | 0.12941 | 0.38424 | 0.28829 | 0.24679
Int Offload | 0.16601 | 0.44256 | 0.29316 | 0.27462

## Slide 28: S/G to Scratchpad
Identify regions to S/G to scratchpad, offload
Demonstrate:
  Able to offload substantial % of integer operations
  Good reuse of data when in scratchpad
  Scratchpad sizes reasonable (L1 sized)
  S/G data less “dense” – can be smarter / more efficient than Cache
Chart: S/G Scratchpad Reuse
| Kripke | hpgmg-ij | hpgmg-ijk | XSBench
 | 8.0524 | 26.8365 | 34.2665 | 3.5582
Chart: S/G Scratchpad Size (KB)
| Kripke | hpgmg-ij | hpgmg-ijk | XSBench
size (B) | 31.9922 | 6.6094 | 55.6094 | 40.1172
Chart: Instruction Offload*
| Kripke | hpgmg-ij | hpgmg-ijk | XSBench
%Reads* | 0.043181 | 0.14729 | 0.17124
%Non-Mem | 0.092128 | 0.046804 | 0.027254 | 0.14845
🙂
🙂
🙂
😐
(☹️)

## Slide 29: Summary
SST provided
  Analysis infrastructure
  S/G Evaluation infrastructure
Quick development
  No need to modify compiler
  Wide range of access patterns identified
Useful basis of collaboration?

## Slide 30: Questions?