## Slide 1: The Structural Simulation Toolkit
Clay Hughes
SST Development Team, Sandia National Laboratories
Architecture Accelerator Lab, Purdue University
SAND2019-14759 PE

## Slide 2: References
Websites
  http://www.sst-simulator.org/
  https://github.com/sstsimulator
Configuration File Format:
  http://sst-simulator.org/SSTPages/SSTUserPythonFileFormat/
Doxygen Documentation:
  http://sst-simulator.org/SSTDoxygen/9.1.0_docs/html/
Developer FAQ:
  http://sst-simulator.org/SSTPages/SSTTopDocDeveloperInfo/
Building SST
  http://sst-simulator.org/SSTPages/SSTBuildAndInstall9dot0dot0SeriesQuickStart/
  http://sst-simulator.org/SSTPages/SSTBuildAndInstall9dot0dot0SeriesDetailedBuildInstructions/

## Slide 3: So many simulators, so little interoperability
Already a rich selection of open-source simulators
But not a solid ecosystem for modeling systems
  Tightly-entangled components make modifications complex
    E.g., assumptions about caching or address mapping pervasive
  Most simulator integrations are ad-hoc, not lasting
  Significant performance problems with tying many simulators together
Wants:
  Enable “mix-and-match” of existing models to create custom systems
  Encourage disentangled models with clean interfaces for swapping functionality
    Bricks not buildings
  Low effort, high performance parallel simulation
  Continuous path from low-fidelity/fast modeling to high-fidelity/slow models

## Slide 4: The Structural Simulation Toolkit
Goals
Create a standard architectural simulation framework for HPC*
Ability to evaluate future systems on DOE/DOD workloads
Use supercomputers to design supercomputers
Status
Parallel framework (SST Core)
Integrated libraries of components (Elements)
Current Release (9.1.0)
  https://sst-simulator.org
  https://github/sstsimulator
Technical Approach
Parallel Discrete Event core
  With conservative optimization over MPI/Threads
Interoperability
  Node and system-scale models
Multi-scale
  Detailed (~cycle) and simple models that interoperate
Open
    Open Core, non-viral, modular
Consortium
“Best of Breed” simulation suite
Combine Lab, Academic & Industry

## Slide 5: The SST Approach
Parallel Discrete-Event Simulator Framework (SST Core)
  Flexible framework enables multitude of custom “simulators”
  Demonstrated scaling to over 512 processors running a million+ components
Comes with many built-in simulation models (SST Elements)
  Processors, memories, networks
Open API
  Easily extensible with new models
  Modular framework
  Open-source core
Time-scale independent core
  Handles Micro-, Meso-, Macro-scale simulations
C++, Python

## Slide 6: SST Architecture
SST Core framework
  The backbone of simulation
  Provides utilities and interfaces for simulation components (models)
    Clocks, event exchange, statistics and parameter management, parallelism support, etc.
SST Element libraries
  Libraries of components that perform the actual simulation
  Elements include processors, memory, network, etc.
    Includes many existing simulators: DRAMSim2, Spike, HMCSim, Ramulator, etc.
Integration Services
MPI and C++ Threads
Component
Component
Component
Component
SST Core

## Slide 7: Running a simulation and code orientation
High-Level View

## Slide 8: Getting and Installing SST
http://www.sst-simulator.org
  Current release source download
  Detailed build instructions including dependencies for Linux & Mac
  Archived tutorial materials
https://github.com/sstsimulator
  Source code checkout
  Master branch – has passed testing
  Devel branch – has passed basic testing

## Slide 9: Building Blocks
SST simulations are comprised of components connected by links
  Every link has a minimum (non-zero) latency
  Components define ports which are valid connection points for a link
Components communicate by sending events over the links
Components can use subcomponents and modules for customizable functionality
Component
Core
Component
Cache
Component
Core
Component
Cache
Component
NoC Router
Component
NoC Router
Link
Latency: 1ns
Link
Latency: 2ns
Link
Latency: 2ns
Link
Latency: 1ns
Link
Latency: 4ns
SubComponent
Prefetcher
Event
Load
Event
Data
Element Library
A collection of components, subcomponents, and/or modules

## Slide 10: SST Code Structure
SST Core and SST Elements are compiled separately
  Element libraries register with the core
  External elements (not part of SST Elements) can also be registered with the core
    Example at github.com/sstsimulator/sst-external-element
  Core maintains a database of registered libraries
    Can query database with sst-info utility
Source code for core:
  sst-core/src/sst/core/
Source code for elements
  sst-elements/src /sst/elements/
  Most elements have a tests/ directory
    Often a good starting point for example configurations
Integration Services
MPI and C++ Threads
Component
Component
Component
Component
SST Core

## Slide 11: Simulating with SST
We’ll walk through how to configure a simulation and then run it
  Available at: https://github.com/sstsimulator/sst-tutorials/tree/master/gt2019
  ( github  sstsimulator  sst-tutorials  gt2019 )
Element libraries in our example simulation
  Miranda - Simple core model that runs generated instruction streams
    Generators produce memory access patterns (SubComponents)
  memHierarchy – Various cache/memory system related subcomponents and modules
    Cache (Component) with coherence protocol SubComponent
    Memory Controller (Component) that loads a memory timing model (SubComponent)
Core
L1 Cache
MemCtrl
2KB, 4-way set associative
2.4GHz, 2 cycle access
64B cache lines
LRU replacement MESI coherence protocol
2.4GHz, issue 2 accesses/cycle
Stream triad generator
Three 1K element arrays A,B,C
Compute C[i] = A[i] + 2*B[i]
 2K reads & 1K writes
50ns constant access latency
1GB capacity
Gen
Mem

## Slide 12: Configuration File: Global SST parameters
Set any global simulation parameters
  End simulation at 100ms if it hasn’t ended already
Other options
  Most are also available as command line arguments to SST
Option | Definition
debug-file | File to print debug output to
heartbeat-period | If set, SST will print a heartbeat message at the specified period
timebase | Units of simulation. Default is picoseconds which enables 2/3 of a year.
partitioner | Partitioner to use for parallel execution
output-partition | File to print partition to
SST Python API
User-defined string
SST argument
sst.setProgramOption(“stopAtCycle”, “100ms”)

## Slide 13: Configuration File: Declare components and links
Components: sst.Component(“name”, “type”)
Links: sst.Link(“name”)
core = sst.Component(“core”, “miranda.BaseCPU”)
cache = sst.Component(“L1”, “memHierarchy.Cache”)
mctrl = sst.Component(“memctrl”, “memHierarchy.MemController”)
link0 = sst.Link(“core_to_cache”)
link1 = sst.Link(”cache_to_memory”)
Component name
Component library.type
Core
Cache
MemCtrl
Link name
SST Python API
User-defined string
SST argument
Gen
Mem

## Slide 14: Configuration File: Configure the components
Parameters: addParams({ “parameter” : “value”, … })
SubComponents: setSubComponent(“slotname”, “type”)
  Recall: SubComponent is a swappable piece of functionality
core.addParams({ “clock” : “2.4GHz” })
Core
Cache
MemCtrl
gen = core.setSubComponent(“generator”, “miranda.STREAMBenchGenerator”)
memory = mctrl.setSubComponent(“backend”, “memHierarchy.simpleMem”)
SST Python API
User-defined string
SST argument
How do I know what the options are? Or even what elements I can pick from?
Gen
Mem

## Slide 15: SSTInfo: Getting component info
sst-info: utility to query element libraries
$ sst-info miranda.BaseCPU
PROCESSED 1 .so (SST ELEMENT) FILES FOUND IN DIRECTORY(s) /home/sst/build/sst-elements/lib/…
Filtering output on Element = “miranda.BaseCPU”
================================================================================
ELEMENT 0 = miranda ()
Num Components = 1
Component 0: BaseCPU
CATEGORY: PROCESSOR COMPONENT
NUM STATISTICS = 17
…
NUM PORTS = 2
PORT 0 = cache_link (Link to Memory Controller)
…
NUM SUBCOMPONENT SLOTS = 2
SUB COMPONENT SLOT 0 = generator (What address generator to load) [SST::Miranda::RequestGenerator]
…
NUM PARAMETERS = 12
PARAMETER 0 = clock (Clock for the base CPU) [2GHz]
…
Optionally filter for a specific library and/or component
Parameter
Definition
“REQUIRED” or default value
Port name
Definition
Slot name
Definition
SubComponent API

## Slide 16: Configuration File: Connecting the components
Declared links and components a couple slides ago…
Connect components: connect(endpoint1, endpoint2)
  Where endpoint is: (component, port, latency)
link0 = sst.Link(“core_to_cache”)
link1 = sst.Link(“cache_to_memory”)
link0.connect(
(core, “cache_link”, “100ps”),
(cache, “high_network_0”, “100ps”) )
link1.connect(
(cache, “low_network_0”, “100ps”),
(mctrl, “direct_link”, “100ps”) )
Endpoint 1
Endpoint 2
Core
Cache
MemCtrl
core = …
cache = …
mctrl = …
Gen
Mem

## Slide 17: Running SST
Usage: sst [options] configFile.py
Common options:
-v ¦ --verbose | Print information about core runtime
--debug-file <filename> | Send debugging output to specified file (default: sst_output)
--partitioner <zoltan ¦ self ¦ simple ¦ rrobin ¦ linear ¦ lib.partitioner.name> | Specify the partitioning mechanism for parallel runs
-n ¦ --num_threads <num> | Specify number of threads per rank
--model-options “<args>” | Command line arguments to send to the Python configuration file
--output-partition <filename> | Write partitioning information to <filename>
--output-dot <filename> --output-xml <filename> --output-json <filename> | Output the configuration graph in various formats to <filename>
Notes: Is this still up to date?

## Slide 18: Running a simulation
Launch simulation
Output
We probably want more information about what happened though
  Enable statistics!
$ sst demo_1.py
Simulation is complete, simulated time: 6.66491 us

## Slide 19: Enabling statistics
Most Components and SubComponents define statistics
Enable statistics in the configuration file
  enableAllStatisticsForAllComponents()
  enableAllStatisticsForComponentType(type)
  enableAllStatisticsForComponentName(name)
  setStatisticLoadLevel(level)
Configure output
  setStatisticOutput(“sst.output_type”)
  setStatisticOutputOptions({“option” : “value”, })
  enableStatisticForComponentName(name, stat)
  enableStatisticForComponentType(type, stat)
$ sst-info memHierarchy.Cache
…
NUM STATISTICS = 51
STATISTIC 0 = CacheHits [Total number of cache hits] (count) Enable Level = 1
STATISTIC 1 = latency_GetS_hit [Latency for read hits] (cycles) Enable level = 1

## Slide 20: Running with statistics enabled
Let’s enable statistics for all components
  Caches have A LOT of statistics so send the output to a CSV file
  Other options: sst.statoutputX where X=
    console
    json
sst.setStatisticOutput(“sst.statoutputcsv”)
sst.setStatisticOutputOptions({ “filepath” : “stats.csv” })
sst.setStatisticLoadLevel(5)
sst.enableAllStatisticsForAllComponents()
    txt
    hdf5

## Slide 21: Running a Simulation – Add Statistics
Copy configuration
Add statistics to new configuration
Launch simulation
Take a minute to look at the statistics
  Can you calculate the L1 memory bandwidth?
$ cp demo_1.py demo_2.py
What should you add?
$ sst demo_2.py

## Slide 22: SST in parallel
SST was designed from the ground up to enable scalable, parallel simulations
Components distributed among MPI ranks/threads
  Link latency controls synchronization rate
MPI Rank 0
MPI Rank 0
MPI Rank 1
MPI Rank 2
MPI Rank 3
Comp0
Comp2
Comp4
Comp6
Comp1
Comp3
Comp5
Comp7
Comp0
Comp2
Comp4
Comp6
Comp1
Comp3
Comp5
Comp7
Same configuration file
# Two ranks
$ mpirun –np 2 sst demo1.py
# Two threads
$ sst –n 2 demo1.py
# Two ranks with two threads each
# This will give a warning since we only
# have 3 components across 4 ranks/threads
$ mpirun –np 2 sst –n 2 demo1.py
Notes: Links handle serialization

## Slide 23: SST Elements: A Tour

## Slide 24: SST Element Libraries
Elements are libraries of related components
  Elements must be registered with the SST core
    Tells SST where to find this set of components
    Includes information on parameters and statistics for each component
SST provides a set of element libraries
  Processor, network, memory, etc.
  Tested for interoperability within and across libraries
  Many are compatible with external “components” such as Ramulator and Spike
    See www.sst-simulator.org for more information
You can also register your own elements

## Slide 25: SST 9.0 Elements
Processors
  Ariel – PIN-based
  Juno – simple ISA processor
  Miranda – pattern generator
  Prospero – trace execution
  GeNSA – Spiking temporal processing unit
Memory Subsystem
  cacheTracer – cache tracing
  Cassini – cache prefetchers
  CramSim – DDR, HBM
  MemHierarchy – caches, directory, memory
  Messier - NVM
  Samba – TLB
  VaultSimC – vaulted stacked memory
Network drivers
  Ember – communication patterns
  Firefly – communication protocols
  Hermes – MPI-like driver interface
  Zodiac – trace based driver
  Thornhill – memory models for Ember sims
Networks/NoCs
  Merlin – flexible network modeling
  Kingsley – mesh NoC
  Shogun – crossbar NoC
Others
  sst-macro – network drivers/network
  scheduler – job scheduling
  simpleSimulation – “car wash” example
  simpleElementExample – many examples
  sst-external-element – example element

## Slide 26: Juno: Simple instruction processor
Executes a program written in simple “assembly”
  32-bit wide instructions with 8 bit op codes
  64-bit integer operations
    ADD, SUB, DIV, MUL,
    AND, OR, XOR, NOT
  Jump by register value (JGT-Zero, JLZ-Zero, J-Zero)
    Jump up to16 bits in either direction from current PC
  Up to 253 user registers
    r0 = PC
    r1 = data start register
Memory
Juno
Instruction Manager
Load/Store Unit
Register File
Processor
Memory
Other
Network/NoC
Network driver

## Slide 27: Ariel: PIN-based processor
Lightweight processor core model
Uses Intel’s PIN tools and XED decoders to analyze binaries
  Runs x86, x86-64, SSE/AVX, etc. binaries
  Supports fixed thread count parallelism (OpenMP, Qthreads, etc.)
Passes instructions to virtual core in SST
Processor
Memory
Other
Network/NoC
Network driver
GPGPU-Sim Integration

## Slide 28: Ariel: Details
Pintool communicates with Ariel via shared memory IPC
  Per-thread FIFO of instructions from pintool to Ariel’s virtual cores
  Backpressure on FIFO halts the binary’s execution
Ariel’s virtual cores
  Memory instruction oriented: execute memory instructions; other ins. single cycle no-ops
  Clocked: Reads instruction stream in chunks but processes on clock
  Does not maintain dependence order or register locations
  Can map virtual-to-physical addresses internally or use external component
Key parameters
  Ops issued/cycle
  Load/store queue size
Uses SST simpleMem interface
  Generates SimpleMemRequests
  Compatible with memHierarchy
Processor
Memory
Other
Network/NoC
Network driver

## Slide 29: Ariel: The Tradeoff
Pros:
  Faster than more complex/pipeline models
  Reasonable approximation for studies on memory system performance
    Especially for heavily memory-bound applications
  Reasonable model of thread interactions
Cons
  Non-deterministic results
    Interactions between pintool, threads, etc.
    Variation is low (O(1%))
  Not compatible with non-x86 binaries
  Reliant on Pin 2.14
    Currently working towards enabling Ariel to be used with other drivers
Processor
Memory
Other
Network/NoC
Network driver

## Slide 30: Prospero: Trace-based processor
Trace-based processor model
  Like Ariel, memory instruction oriented
    Reads memory ops from a file and passes to the simulated memory system
  “Single core” but can use multiple trace files to emulate threaded or MPI applications
  Supports arbitrary length reads to account for variable vector widths
  Performs “first touch” virtual to physical mapping
Comes with Prospero Trace Tool to generate traces
  Or can generate your own and translate to Prospero’s format
Processor
Memory
Other
Network/NoC
Network driver

## Slide 31: Prospero: The Tradeoff
Pros
  Faster than Ariel*
    Provided you can get a trace
Cons
  Traces can be very large
    Requires good I/O system to store and read the trace
  Traces are less flexible than actual execution
    Capture a single execution stream using a single application input
Processor
Memory
Other
Network/NoC
Network driver

## Slide 32: Miranda: Pattern-based processor
Extremely light-weight processor model
  Generates memory address patterns
  Supports request dependencies
Library patterns
  Strided accesses (single stream)
    Forward and reverse strides
  Random accesses
  GUPS
  STREAM benchmark
    In-order & out-of-order CPU
  3D stencil
  Sparse matrix vector multiply (SpMV)
  Copy (~array copy)
  Stake interface to the Spike RiscV simulator
Processor
Memory
Other
Network/NoC
Network driver

## Slide 33: Miranda: The tradeoffs
Pros
  Very lightweight – no binary, no trace
  Good for applications whose address patterns are predictable
    e.g., not much pointer-chasing
  Models instruction dependences
Cons
  Need a generator for the memory pattern of interest
    Requires a good understanding of the pattern
Processor
Memory
Other
Network/NoC
Network driver

## Slide 34: MemHierarchy: Memory system
Collection of interoperable memory system elements
  Caches
  Directories
  Memory controllers
    Interfaces to memory models (DDR, HBM, HMC, NVM, etc.)
  Scratchpads
  NoC (network-on-chip) interfaces
  Buses
Components are cycle-accurate/cycle-level
Capable of modeling modern cache and memory subsystems
Processor
Memory
Other
Network/NoC
Network driver

## Slide 35: MemHierarchy: Cache modeling
Highly configurable
  Arbitrary hierarchy depth, flexible topologies
  Cache inclusivity, coherence, private/shared, etc. configurable
  Single- and multi-socket configurations
  Prefetch via Cassini element library
Data movement
  Components support direct, bus, and on-chip network (NoC) communication
Event types: read/write, atomics, LLSC, noncacheable, custom memory, etc.
Processor
Memory
Other
Network/NoC
Network driver

## Slide 36: MemHierarchy: Memory modeling
Interface to memory is the MemController
MemControllers implement backends
  Timing model for memory controller with a link to memory
  Timing model for memory controller and memory
  Interface to another component(s) that does the memory controller/memory timing
    In this case just translates request formats
  Wrapper for an external/non-native-SST component
    Ramulator, DRAMSim2, etc.
Support custom memory instructions
  Including ability to do cache shootdowns for coherence maintenance
Processor
Memory
Other
Network/NoC
Network driver

## Slide 37: MemHierarchy: Memory modeling
Memory controller
  Manages data values if needed (backing store)
  Facilitates custom memory commands
    Including cache shootdowns for coherence maintenance
  Passes events to memory backend subcomponent
Backend: the “real” memory controller and/or memory
  Implementations
    Memory controller and model itself
    Memory controller with interface to a memory component
    Interface to another memory controller/memory component
    Wrapper to an external simulator
Memory Controller
Backend
Backing store
Custom command handler
To memory component (optional)
Processor
Memory
Other
Network/NoC
Network driver

## Slide 38: MemHierarchy: SST 9.1 backends
Memory (external)
  CramSim (DDR, HBM)
  DRAMSim2 (DDR)
    PagedMulti – 2-level memory variant
  FlashDIMMSim (FLASH)
  HMCSim/GoblinHMC (HMC)
  HBMDRAMSim2 (HBM)
    HBMPagedMulti – 2-level memory variant
  Messier (NVRAM)
  Ramulator (DDR, HBM, HMC)
  SimpleDRAM (DDR)
  SimpleMem (constant latency)
  TimingDRAM (DDR)
  VaultSimC (HMC-like)
Plus a few that can be used with other backends to reorder requests, add latency, etc.
Processor
Memory
Network/NoC
Network driver
Other

## Slide 39: Running a Simulation – Add Components, L2 Cache
Copy configuration
Add an L2 cache between L1 and memory to new configuration
  What parameters are available for an L2 cache?
  What are appropriate values for the parameters?
Launch simulation
  How did this affect your overall simulated time?
  How did this affect traffic to and from your backing store?
$ cp demo_2.py demo_3.py
What should you add?
$ sst demo_3.py

## Slide 40: Running a Simulation – Switch Components, Timing DRAM
Copy configuration
Switch the simpleMem subcomponent for timingDRAM
Launch simulation
  How do your results differ from the run with simpleMem?
$ cp demo_3.py demo_4.py
What should you change? Remember that sst-info is your pal!
$ sst demo_4.py

## Slide 41: Merlin: Network simulator
Low-level networking components that can be used to simulate high-speed networks (machine level) or on-chip networks
Capabilities
  High radix router model (hr_router)
  Topologies – mesh, n-dim tori, fat-tree, dragonfly
Many ways to drive a network
  Simple traffic generation models
    Nearest neighbor, uniform, uniform w/ hotspot, normal, binomial
  MemHierarchy
  Lightweight network endpoint models (Ember – coming up next)
  Or, make your own
Processor
Memory
Network/NoC
Network driver
Other

## Slide 42: Merlin: Organization
PC
PC
PC
PC
PC
PC
PC
PC
Topology
XBAR
Router
PC = PortControl
LC
LC = LinkControl
TrafficGen
TestNIC
User Logic
NIC
Processor
Memory
Network/NoC
Network driver
Other

## Slide 43: Kingsley: Mesh simulator
Network-on-chip model; mesh configuration
Similar to Merlin but:
  No input queuing at routers
  Mesh topology only
  Not all ports need to be populated
  Possible to instantiate multiple unconnected networks
    Multiple physical networks for coherence (e.g., request/response/ack/forward)
    Kingsley NoC + Merlin/Kingsley system network
Processor
Memory
Network/NoC
Network driver
Other
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
NIC
Interconnect

## Slide 44: Ember: Network Traffic Generator
Light-weight endpoint for modeling network traffic
  Enables large-scale simulation of networks where detailed modeling of endpoints would be expensive
Packages patterns as motifs
  Can encode a high level of complexity in the patterns
  Generic method for users to extend SST with additional communication patterns
Intended to be a driver for the Hermes, Firefly, and Merlin communication modeling stack
  Uses Hermes message API to create communications
  Abstracted from low-level, allowing modular reuse of additional hardware models
Processor
Memory
Network/NoC
Network driver
Other

## Slide 45: Ember: Overview
User
Binary
Ember Engine
Hermes API
Firefly
Merlin Network
Ember Motif
Message Passing Semantics
Collectives, Matching, etc.
Packetization and Byte Movement Engine
Generates packets and coordinates with network
Flit Level Movement, Routing, Delivery
Moves flits across network, timing, etc.
Event to Message Call, Motif Management
Handles the tracking of the motif
High Level Communication Pattern and Logic
Generates communication events
Processor
Memory
Network/NoC
Network driver
Other

## Slide 46: Ember: Motifs
Motifs are lightweight patterns of communication
  Tend to have very small state
  Extracted from parent applications
  Models as an MPI program (serial flow of control)
    Many motifs acting in the simulation create the parallel behavior
Example motifs
  Halo exchanges (1, 2, and 3D)
  MPI collections – reductions, all-reduce, gather, barrier
  Communication sweeping (Sweep3D, LU, etc.)
Processor
Memory
Network/NoC
Network driver
Other

## Slide 47: Ember: Motifs (continued)
The EmberEngine creates and manages the motif
  Creates an event queue which the motif adds events to when probed
  The Engine executes the queued events in order, converting them to message semantic calls as needed
  When the queue is empty, the motif is probed again for events
Events correspond to a specific action
  E.g., send, recv, allreduce, compute-for-a-period, wait, etc.
Processor
Memory
Network/NoC
Network driver
Other

## Slide 48: Firefly: Network traffic
Purpose: Create network traffic, based on application communication patterns, at large scale
  Enables testing the impact of network topologies and technologies on application communication at very large scale
Scales to 1 million nodes
Supports multiple “cores” per Node
  Interaction between cores limited to message passing
Supports space sharing of the network
  Multiple “apps” running simultaneously
Processor
Memory
Network/NoC
Network driver
Other

## Slide 49: Firefly: Simulating large networks
A network node consists of
  Driver (the “application”)
  NIC
  Router
Nodes are connected together via routers to form a network
  Fat tree, torus, etc.
Firefly is the interface between the driver and the router
  Message passing library  Firefly Hades
  NIC  Firefly NIC
Ember
(driver)
Firefly Hades
Firefly NIC
Merlin Router
Processor
Memory
Network/NoC
Network driver
Other

## Slide 50: Scheduler: Job scheduling
Models HPC system-wide job scheduling
Three components
  Sched: schedules and allocates resources for a stream of jobs
  Node: runs scheduled jobs on their allocated resources
  FaultInjection: injects failures onto the resources
The scheduler can be a stand-alone element library
  The schedComponent and nodeComponent must be used together
  The faultInjectionComponent is optional
Can be used with Ember/Firefly/Merlin stack
  Examine topology aware scheduling and allocation
Processor
Memory
Network/NoC
Network driver
Other

## Slide 51: Other Libraries
More information on these and other element libraries and external components is available on the wiki
  www.sst-simulator.org

## Slide 52: Viewing Configuration Graph
Let’s take a look at how SST views our system
Re-run demo_4 but add a command to dump the configuration graph
This gives you a GraphViz formatted file
Is this how you expected your system to look?
With this in mind, let’s add a second Miranda core…
$ sst --output-dot=graph_demo_4.dot demo_4.py
$ dot –Tpdf graph_demo_4.dot –o graph_demo_4.pdf
$ evince graph_demo_4.pdf

## Slide 53: Running a Simulation – Add Components, Second Miranda
Copy configuration
Add an a second Miranda generator
  What else might you need?
Dump the wiring diagram to verify the model
Launch simulation
$ cp demo_4.py demo_5.py
$ sst demo_5.py
How about another L1 cache?
How are you going to wire everything together? How about a bus?

## Slide 54: Running a Simulation – Add Components, Second L2
Copy configuration
Add L2 cache and move both above the bus
Launch simulation
$ cp demo_5.py demo_6.py
$ sst demo_6.py

## Slide 55: Running a Simulation – Add Components, Second Memory
Copy configuration
Add an a second L2 and memory controller
  Think carefully about how addressing should will work…
Launch simulation
$ cp demo_6.py demo_7.py
$ sst demo_7.py
Can you still use a bus?
Can the talk directly to the memory controller?

## Slide 56: Running a Simulation – Add Components, Second Memory
Swap the bus component for the shogun component
Add directory controllers before the memory
shogun_xbar = sst.Component("shogunxbar", "shogun.ShogunXBar")
shogun_xbar.addParams({
"clock" : "1.0GHz",
"port_count" : 4,
"verbose" : 0
})
dirctrl = sst.Component("dirctrl_" + str(cache_id), "memHierarchy.DirectoryController")
dirctrl.addParams({
"coherence_protocol" : "MESI",
"entry_cache_size" : "32768",
"addr_range_end" : endAddr,
"addr_range_start" : startAddr,
"interleave_size" : "256B",
"interleave_step" : str(numLLC * 256) + "B",
})
dc_cpulink = dirctrl.setSubComponent("cpulink", "memHierarchy.MemNIC")
dc_memlink = dirctrl.setSubComponent("memlink", "memHierarchy.MemLink")
dc_cpulink.addParams({
"group" : 3,
})
dc_linkctrl = dc_cpulink.setSubComponent("linkcontrol", "shogun.ShogunNIC")

## Slide 57: Getting help and extending SST

## Slide 58: Extending SST
SST was designed for extensibility
  Components/subcomponents can be added without touching SST Elements
    Example: write a new prefetcher and have memH caches use it  no changes to memHierarchy
  SST-Core APIs are stable  one year deprecation period
    Element APIs may be less so but generally try to keep them consistent
  Many users start with SST Elements and then build their own customized libraries
    Partially or completely replacing SST Element functionality
Many approaches to using SST
  Core only: Write your own components from scratch
  Start from existing Elements and replace components/subcomponents to meet your needs
  Wrap existing simulators and insert as components or subcomponents

## Slide 59: Extending SST: Resources
Example element library
  Components demonstrating links, ports, clocks, event handling, etc.
  sst-elements/src/sst/elements/simpleElementExample/
simpleSimulation
  Simulates a car wash (a little more complex than example elements)
Example external element library
  Demonstrates building and registering a new element library
  https://github.com/sstsimulator/sst-external-element
Website
  Getting Started Extending SST (a little out of date)
  Building Element Libraries outside SST source tree
  Past tutorial material (under Downloads)
  sst-simulator.org/SST-website API documentation

## Slide 60: Finally: Getting help
SST wiki contains lots of information (www.sst-simulator.org)
  Downloading, installing, and running SST
  Element libraries and external components
  Guides for extending SST
  Information on APIs
  Information about current development efforts
  Past tutorial slides and exercises
SST Github
  Current development
  Issues track user questions as well as development plans, bugs, etc.

## Slide 61: Part 1 wrap-up
SST is a parallel, flexible simulation framework
  Can simulate many systems at many granularities
  Capable of simulating modern architectures
  Modular design for extensibility
Please keep us posted on your uses of SST as well as any capabilities you’ve added or would like to see added
The SST team wants to help you!
Documentation?
Examples?
Kittens?

## Slide 62: Backup

## Slide 63: Demo_5 Wiring

## Slide 64: Running a Simulation – Add Components, Simple Node
Copy configuration
Add the components to create a simple node
  Each PE has a Miranda generator and an L1
  The two memory nodes should use timingDRAM
  How should you connect everything?
Launch simulation
$ cp demo_6.py demo_7.py
$ sst demo_7.py