## Slide 1: ERAS: Enabling Integration of Real-World Intellectual Properties in Architectural Simulators
The SST and SACA Teams (Sandia, NC State)

## Slide 2: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work

## Slide 3: Overview
Frontend HDLs
Tool Flow
Generated C-model
Integrable Module
ERAS
General WorkFlow: HDL → FIRRTL → ESSENT → Parser → SST
Goals:
                Support several types of Low-level IPs
                Easy, customizable workflow

## Slide 4: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work

## Slide 5: Why ERAS ?
Analyze impact on system level behavior with realistic cycle-accurate low level IP model
Analyze impact of system level changes on external IP integrated with SST
Extensibility to an extent that full system is modelled through only realistic IPs
SST system simulation
Impact on External IP

## Slide 6: Why ERAS ?
RTL Model
SST
Component
SST
Component
SST
Component
SST
Component
SST
Component
SST
Component
SST
Component
SST Component
Analyze impact on system level behavior with realistic cycle-accurate low level IP model
Analyze impact of system level changes on external IP integrated with SST
Extensibility to an extent that full system is modelled through only realistic IPs

## Slide 7: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work

## Slide 8: Framework Highlight
Designer provides necessary information to the Parser
Parser interprets the information and invoke necessary blocks of the generic component, referred as Osseus, to integrate the C-model with SST
ISPASS 2023 Tutorial

## Slide 9: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work
ISPASS 2023 Tutorial

## Slide 10
Parser Input Requirements
Osseous APIs (Input Port spec and wrapper code spec)
  Clock Handlers – Calls eval() that is clocked each cycle
  memHandler – APIs generating & serving mem requests
  Memory manager – Address translations
  Event Handlers (e.g., interface handlers of AXI)
  Element information (SST_ELI_*)
      SST Parameters, Statistics, additional ports, slots
      Describe parameters from Python Config file
  Boilerplate code (init(), setup(), finish() APIs)
    Initialize or load test vector/binary files
    Creating testbench consumed as x86 binary
ISPASS 2023 Tutorial

## Slide 11: Input Stimulus
Testbench/x86 binary or mem loadable Hex file
  RTL Simulation requires input stimulus
  TestBench to update RTL signals are written in C and compiled using gcc / g++
  Custom APIs to offload computation to RTL model are created (e.g. start_RTL_sim(), update_RTL_sig())
  Independent RTL requires loading Hex file to memHierarchy (e.g. RISC-V CPU)
ISPASS 2023 Tutorial

## Slide 12: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work
ISPASS 2023 Tutorial

## Slide 13: Handlers
Establish Link between SST world and C-model supported interfaces/ interconnect for inter-component communication.
Autogenerated code invoked by the parser on demand.
Handler records transaction statistics to evaluate performance impacts.
ISPASS 2023 Tutorial

## Slide 14: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work
ISPASS 2023 Tutorial

## Slide 15: Summary
Quick and seamless integration of low-level detailed simulation with highly modular, parallelizable architectural simulator such as SST facilitate:
  Fast evaluation of performance impact of designed IP on abstract high level architecture models.
  System level study of detailed simulation to incorporate early design changes.
  Design space exploration driven by real world IP constraints.
  Save significant efforts in modelling architectural components through exploiting reusability of existing models in SST.
ISPASS 2023 Tutorial

## Slide 16: Outline
Overview
Motivation
Framework Highlight
Parser
Handlers
Summary
Future Work
ISPASS 2023 Tutorial

## Slide 17: Future Work
Instantiate and interface multiple Osseus components.
Take out the dependency on existing SST cores (e.g. Ariel) to run system-level simulation with Osseous.
ISPASS 2023 Tutorial

## Slide 18: Demo
Example 1: Counter circuit
  Workflow and test setup
  Verilog vs SST testbench
Example 2: RISCV-Mini
  AXI Handler
  Design space exploration use case
Summary
ISPASS 2023 Tutorial

## Slide 19: Example 1: Workflow and test setup
The Verilog/Chisel model of the design is translated to FIRRTL which is then used to generate the C-model using Essent1
The testbench is a C file which is compiled to a x86 binary and executed by Ariel CPU using PIN tool2.
The Ariel CPU writes the signal values received from the testbench to the Memhierarchy and notifies the DUT.
The DUT fetches the latest signal values from the Memhierarchy and executes for cycles as determined by the testbench.
Figure 1: ERAS framework workflow and test setup
1: S. Beamer, "A Case for Accelerating Software RTL Simulation," in IEEE Micro, vol. 40, no. 4, pp. 112-119, 1 July-Aug. 2020, doi: 10.1109/MM.2020.2997639.
2: Pin - A Dynamic Binary Instrumentation Tool (intel.com)
ISPASS 2023 Tutorial

## Slide 20: Example 1: Counter circuit
Figure 3: Chisel
Figure 4: Verilog
Figure 5: FIRRTL
Figure 6: C-model
Figure 2: Circuit design
Essent
ISPASS 2023 Tutorial

## Slide 21: Example 1: Test bench in Verilog and SST
Figure 9: SST test log
Figure 8: Verilog testbench
Rtlmodel-rtlaximodel-> Updated Rtl Params is: 1
Rtlmodel->sim cycles: 4
Rtlmodel->update inp: 1
Rtlmodel->update ctrl: 1
Rtlmodel->input sigs: 0x0<U1>Rtlmodel->input sigs: 0x1<U1>Rtlmodel->input sigs: 0x1<U4>
io tot: 0x00<U8>
io tot: 0x01<U8>
io tot: 0x02<U8>
Performing update on RTL params
Store to mem called
Store to mem finished
io tot: 0x03<U8>ArielComponent[arielcore.cc:1539:processNextEvent]
ArielRTLEvent is being issuedRtlmodel-rtlaximodel->
VecshiftReg RTL Event handle called
Rtlmodel-rtlaximodel->
Rtlmodel-rtlaximodel-> Updated Rtl Params is: 1
Rtlmodel->sim cycles: 4
Rtlmodel->update inp: 1
Rtlmodel->update ctrl: 1
Rtlmodel->input sigs: 0x0<U1>Rtlmodel->input sigs: 0x1<U1>Rtlmodel->input sigs: 0x2<U4>
io tot: 0x04<U8>
io tot: 0x06<U8>
io tot: 0x08<U8>
io tot: 0x0a<U8>Rtlmodel-rtlaximodel-> OKToEndSim, TickCount 4ArielComponent[arielcore.cc:1400:handleRtlAckEvent]
Ariel received Event from RTL. Generating Read Request
Figure 10: Verilog test output
Figure 7: SST testbench
ISPASS 2023 Tutorial

## Slide 22: Example 2: Riscv-Mini & AXI handler
Figure 11: Riscv-Mini microarchitecture
Riscv-Mini3 is a RISC-V 3-stage pipeline written in Chisel.
The package comes with a simple inbuilt memory manager. It loads the binary to the memory which has a fixed access latency of 1 cycle.
In this example, we replace the in-built memory manager with SST’s memhierarchy model.
The Riscv-Mini CPU interfaces with memory manager using AXI4. However, SST’s memhierarchy model doesn’t have an inbuilt AXI interface.
3: https://github.com/ucb-bar/riscv-mini
ISPASS 2023 Tutorial

## Slide 23: Example 2: Riscv-Mini & AXI handler (cont’d)
Figure 12: AXI Handler
The AXI handler acts as a slave device which translates read/write requests received over AXI bus to SST events to read/write data from the memhierarchy.
The AXI handler synchronizes the updating of bus signals and communicating SST events.
A benchmark (quick sort) is loaded to memhierarchy and executed on the Riscv-Mini CPU to analyze the IPC for different L1 cache configurations.
ISPASS 2023 Tutorial

## Slide 24: Design space exploration of L1 cache with Riscv-Mini CPU RTL
Config 1
cache size : 2 KB
cache type : inclusive
coherence protocol : MSI
replacement policy : lru
associativity : 2
access latency cycles : 1
cache line size : 64
Chart: 
| Config 1 | Config 2 | Config 3 | Config 4
IPC | 0.71213 | 0.71345 | 0.69032 | 0.66775
Config 2
cache size : 32 KB
cache type : inclusive
coherence protocol : MSI
replacement policy : lru
associativity : 4
access latency cycles : 4
cache line size : 64
Config 3
cache size : 64 KB
cache type : inclusive
coherence protocol : MSI
replacement policy : lru
associativity : 8
access latency cycles : 6
cache line size : 64
Config 4
cache size : 128 KB
cache type : inclusive
coherence protocol : MSI
replacement policy : lru
associativity : 16
access latency cycles : 8
cache line size : 64
ISPASS 2023 Tutorial

## Slide 25: Contributors
Sandia National Laboratories
  C. Hughes, A. Rodrigues, G. Voskuilen, K. S. Hemmert, S. D. Hammond, B. Feinberg
  Center for Computing Research
  {chughes, afrodi, grvosku, kshemme, sdhammo, bfeinbe}@sandia.gov
North Carolina State University
  S. K. Chunduru, S. Nema, M. Ambati, R. Razdan, J. Kirschner, D. Adak, H. Lee, A. Awad
  Secure and Advanced Computer Architecture Lab
  {schundu2, snema, mambati, rrazdan2, dadak, hyokeun_lee, jkirsch, ajawad}@ncsu.edu
ISPASS 2023 Tutorial

## Slide 26: Thank You
ISPASS 2023 Tutorial