## Slide 1: GPGPU-Sim Overview
Mengchi Zhang, Purdue University
Clay Hughes, Gwen Voskuilen, Sandia National Laboratories
Mengchi Zhang, Purdue University
09/22/2019
SAND2019-11321 C

## Slide 2: Welcome!
Part 1: Introduction to SST 8:45 - 10:15
  SST Overview
    Demos: Running a simple simulation; Enabling statistics; Running in parallel
  SST Element Libraries: A tour
Break 10:15 - 10:45
Part 2: GPGPU-Sim 10:45 – 11:30
  GPGPU-Sim Overview
  New Features
Part 3: The SST/GPGPU-Sim Integration 11:30 - 12:00
Lunch 12:00 - 1:30
SST Exercises 1:30 - 3:00
Break 3:00 - 3:30
GPGPU-Sim Exercises 3:30 - 5:00

## Slide 3: Outline
GPGPU-Sim Introduction
  GPU and programming model
  Functional model
  Performance model
  GPUWattch: power model
New Features in GPGPU-Sim
  Volta model
  Run closed source libraries
  Tensor Core
  Run CUTLASS library
Notes: Description provided in ASC CSSE Milestone 6812.
Prior to this milestone, SST lacked the capability to model any external accelerator. We are now able to model a GPU accelerator in detail and analyze application and system behavior in fine detail.

## Slide 4: Acknowledgements
Some slides are credited to GPGPU-Sim Micro Tutorial 2012
Some data and figures are credited to papers below:
  Akshay Jain, Mahmoud Khairy, Timothy G. Rogers, A Quantitative Evaluation of Contemporary GPU Simulation Methodology. SIGMETRICS 2018
  Mahmoud Khairy, Jain Akshay, Tor Aamodt, Timothy G Rogers, Exploring Modern GPU Memory System Design Challenges through Accurate Modeling, arXiv:1810.07269, ( and ISPASS 2019 poster)
  Jonathan Lew, Deval Shah, Suchita Pati, Shaylin Cattell, Mengchi Zhang, Amruth Sandhupatla, Christopher Ng, Negar Goli, Matthew D. Sinclair, Timothy G. Rogers, Tor M. Aamodt, Analyzing Machine Learning Workloads Using a Detailed GPU Simulator, arXiv:1811.08933, ( and ISPASS 2019 poster)
  Md Aamir Raihan, Negar Goli, Tor Aamodt, Modeling Deep Learning Accelerator Enabled GPUs, ISPASS 2019
We thank all contributors to GPGPU-Sim
All new features are based on the dev branch of GPGPU-Sim: https://github.com/gpgpu-sim/gpgpu-sim_distribution/tree/dev
Notes: Description provided in ASC CSSE Milestone 6812.
Prior to this milestone, SST lacked the capability to model any external accelerator. We are now able to model a GPU accelerator in detail and analyze application and system behavior in fine detail.

## Slide 5: Outline
GPGPU-Sim Introduction
  GPU and programming model
  Functional model
  Performance model
  GPUWattch: power model
New Features in GPGPU-Sim
  Volta model
  Run closed source libraries
  Tensor Core
  Run CUTLASS library
Notes: Description provided in ASC CSSE Milestone 6812.
Prior to this milestone, SST lacked the capability to model any external accelerator. We are now able to model a GPU accelerator in detail and analyze application and system behavior in fine detail.

## Slide 6: GPU Introduction
GPU = Graphics Processing Unit
  Optimized for Highly Parallel Workloads
  Highly Programmable
  Heterogeneous computing
NVidia Tesla GV100: 80 Stream Multiprocessors(SMs)
  Each SM has 64 INT32, 64 FP32, 32 FP64, 8 Tensor core
Notes: Completion criteria for ASC CSSE Milestone 6812.
Please see the last slide on how we have met each of these criteria.

## Slide 7: GPGPU Programming model evolution
GPGPU programming model:
  CUDA and OpenCL
  Support more features with newer architectures
CUDA
OpenCL
CUDA 1.X
C compiler
(Tesla)
2007
CUDA 3.X
C++ compiler
(Fermi)
2010
2014
2017
CUDA 4.X
C++ new/delete
No-copy system memory
CUDA 6.X
Unified memory
Dynamic Parallelism
cuDNN
(Kepler, Maxwell)
CUDA 9.X
Cooperative groups
MPS
CUTLASS
Tensor core operation
(Volta)
OpenCL 1.0
C99 support
2008
OpenCL 2.1
C++14
SPIR-V
for Vulkan
subgroup
2015
OpenCL 2.0
Shared virtual memory
Nested Parallelism
Pipe
2013
2019
CUDA 10.X
CUDA Graphs
(Turing)
OpenCL 1.2
Device Partition
Built-in kernels
2011
OpenCL 2.2
C++14
SPIR-V 1.1
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 8: GPU Microarchitecture1
NVidia GV100:
  Hierarchical compute unit: SM=>TPC=>GPC=>GPU
  Multi-level memory: L1/shmem=>L2=>HBM
  GPGPU-Sim simulator models components above
[1]Volta Whitepaper. https://images.nvidia.com/content/volta-architecture/pdf/volta-architecture-whitepaper.pdf
Notes: Completion criteria for ASC CSSE Milestone 6812.
Please see the last slide on how we have met each of these criteria.

## Slide 9: GPGPU-Sim Introduction
GPGPU-Sim
  Widely used GPU simulator in the research community (1300+ citations).
  The third most cited simulator in computer architecture field (after GEM5(+GEMS) and SimpleScalar)
Functional model
  Virtual ISA (vISA)
  Machine ISA (mISA)
Performance model
  Model microarchitecture timing relevant to GPU compute
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 10: GPGPU-Sim Introduction
GPGPU-Sim simulates kernel
  Transfer data to GPU memory
  GPU kernels runs on GPGPU-Sim:
    Reports statistics for the kernels
  Transfer data back to CPU memory
Time
GPU HW
CPU
Async. Kernel Launch
Done
GPU HW
Done
CPU
GPU HW
Sync. Kernel Launch
Done
CPU
Blocking
GPGPU-Sim
GPGPU-Sim
GPGPU-Sim
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 11: Functional model
Single Instruction Multiple Thread(SIMT):
  SIMD + multithreading
  Grid, Block, Warp, Thread
Virtual ISA vs. Machine ISA
  vISA: PTX = Parallel Thread eXecution: virtual ISA defined by Nvidia
  mISA: SASS = Native ISA for Nvidia GPUs
  GPGPU-Sim use PTXPlus to represent SASS
    1:1 mapping from SASS to PTXPlus
GPGPU-Sim supports:
  PTX for new architectures(CUDA 10): new, inaccurate, well documented
  SASS for architecture before Fermi(SM_1.X): old, accurate, less documented

## Slide 12: Performance model
GPGPU-Sim models timing
  SIMT Core
  Caches and texture/constant/shared memory
  Interconnection network(Booksim)
  DRAM(GDDR5/HBM)
DO NOT model
  Graphic Specific Hardware

## Slide 13: GPUWattch: Power model
Estimate power consumed by the GPU according to the timing behavior
Ideal for evaluating fine-grained power management mechanisms
Validated with power measurements from GV100
Modified McPAT
Modifications: Specific micro-architectural components
GPGPU-Sim
Modifications: Add required performance counters
A Comprehensive Framework for Performance and Energy Optimization Research
Interface
Interface
Static Power
Dynamic Power
Detailed Power Stats
Detailed Performance Stats
Feedback-driven Optimizations
Performance counters
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 14: GPUWattch: Power model
Correlation for GV100
  Coefficient of 0.8
  Average relative error of (95% confidence interval)
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 15: Outline
GPGPU-Sim Introduction
  GPU and programming model
  Functional model
  Performance model
  GPUWattch: power model
New Features in GPGPU-Sim
  Volta model
  Run closed source libraries
  Tensor Core
  Run CUTLASS library
Notes: Description provided in ASC CSSE Milestone 6812.
Prior to this milestone, SST lacked the capability to model any external accelerator. We are now able to model a GPU accelerator in detail and analyze application and system behavior in fine detail.

## Slide 16: New Feature: Volta Model Motivation
ISA cycle correlation1 before new Volta model2
  For Pascal Titan X
[1] Akshay Jain, Mahmoud Khairy, Timothy G. Rogers, A Quantitative Evaluation of Contemporary GPU Simulation Methodology. SIGMETRICS 2018
[2] Mahmoud Khairy, Jain Akshay, Tor Aamodt, Timothy G Rogers, Exploring Modern GPU Memory System Design Challenges through Accurate Modeling, arXiv:1810.07269
Benchmark | Means Abs Error |  | Correlation | 
 | vISA | mISA | vISA | mISA
Compute Intensive | 43.3% | 21.9% | 91.1% | 99.0%
Cache Sensitive | 104.8% | 100.4% | 81.2% | 82.0%
Memory Sensitive | 31.6% | 29.8% | 96.0% | 95.1%
Compute Balanced | 58.5% | 70.7% | 96.1% | 93.5%
Result
  Compute intensive: mISA > vISA
  Cache sensitive: both show inaccurate cache model
  Memory sensitive(streaming): not related to cache model
  Compute balanced: vISA > mISA
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 17: New features: Volta model1
Fermi-based Model
[1] Mahmoud Khairy, Jain Akshay, Tor Aamodt, Timothy G Rogers, Exploring Modern GPU Memory System Design Challenges through Accurate Modeling, arXiv:1810.07269
Instruction Cache
Warp
Scheduler
Register File
(16 banks)
Warp
Scheduler
SFU
Exec Units
SP
SP
L1D cache/Shared Memory
Programmable-specified cache
L2 cache
GDDR5 Model
Fermi coalescer
SIMT Core
Memory Hierarchy
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 18: New features: Volta model1
Volta-based Model
[1] Mahmoud Khairy, Jain Akshay, Tor Aamodt, Timothy G Rogers, Exploring Modern GPU Memory System Design Challenges through Accurate Modeling, arXiv:1810.07269
Instruction Cache
Warp
Scheduler
Register File
Exec Units
L1D Cache / Shared Memory
+Sectored, +Adaptive cache (128 KB),
+Streaming cache +Banked
L2 Cache
+Sectored, +memory copy engine model
+New Lazy_Fetch_on_Read write policy,
+partition-camping-aware hashing
HBM
+ HBM Model, +dual-bus interface
+ Read/Write buffers
Volta coalescer (8 threads coalescer)
SIMT Core
Memory Hierarchy
SP
DP
SFU
INT
Warp
Scheduler
Warp
Scheduler
Warp
Scheduler
Tensor
Register File
Exec Units
SP
DP
SFU
INT
Tensor
Register File
Exec Units
SP
DP
SFU
INT
Tensor
Register File
Exec Units
SP
DP
SFU
INT
Tensor
Subcore model
disaggregate RF
(2 banks)
+DP, INT, Tensor
High-bandwidth Memory
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 19: Hardware correlation for Volta model1
Statistic | Means Abs Error |  | Correlation | 
 | Old Model | New Model | Old Model | New Model
Execution Cycles | 68% | 27% | 71% | 96%
L1 Reqs | 48% | 0.5% | 92% | 100%
L1 Hit Ratio | 41% | 18% | 89% | 93%
L2 Reads | 66% | 1% | 49% | 94%
L2 Writes | 56% | 1% | 99% | 100%
L2 Read Hits | 80% | 15% | 68% | 81%
DRAM Reads | 89% | 11% | 60% | 95%
7X error reduction
in DRAM reads
1% error in L2 behavior
(66x read error reduction)
2.5X error reduction
in exec time
[1] Mahmoud Khairy, Jain Akshay, Tor Aamodt, Timothy G Rogers, Exploring Modern GPU Memory System Design Challenges through Accurate Modeling, arXiv:1810.07269
0.5% error in L1 reqs
(96x reqs error reduction)
SIMT Core
Memory Hierarchy
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 20: Run closed source model1
Run applications with cuDNN/cuBLAS
  Static linking closed source libraries
  LeNet for MNIST using cuDNN/cuBLAS
CUDA API layer
Application
CUDA runtime API layer
CUDA runtime API
Functional model
Performance model
static cuDNN library
Executable
static cuBLAS library
CUDA runtime API
GPGPU-Sim
[1] Jonathan Lew, Deval Shah, Suchita Pati, Shaylin Cattell, Mengchi Zhang, Amruth Sandhupatla, Christopher Ng, Negar Goli, Matthew D. Sinclair, Timothy G. Rogers, Tor M. Aamodt Analyzing Machine Learning Workloads Using a Detailed GPU Simulator, arXiv:1811.08933
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 21: Tensor Core in GV100
Accelerate FP operations
8 Tensor Core/SM
Each perform 64 FP FMA/clock
512 FMA/clock/SM
Or 1024 FP ops/clock/SM
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 22: Tensor Core in Tesla Titan V1
Standard deviation of less than 5%
99.60% IPC correlation
GPGPU-Sim shows higher perf than HW as matrix size increase
[1] Md Aamir Raihan, Negar Goli, Tor Aamodt, Modeling Deep Learning Accelerator Enabled GPUs, ISPASS 2019
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 23: Run CUTLASS library
Combine CUTLASS, tensor core1, and volta model2
Correlation: using Deepbench training/inference test from real scenario
[1] Md Aamir Raihan, Negar Goli, Tor Aamodt, Modeling Deep Learning Accelerator Enabled GPUs, ISPASS 2019
[2] Mahmoud Khairy, Jain Akshay, Tor Aamodt, Timothy G Rogers, Exploring Modern GPU Memory System Design Challenges through Accurate Modeling, arXiv:1810.07269
Chart: Hardware
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 24: Summary
GPGPU-Sim:
  Simulates GPU compute unit and memory hierarchies.
  an evolutional simulator for new features in CUDA and GPUs.
    actively including new features
GPGPU-Sim with SST:
  GPGPU-Sim brings promising GPU model to SST
  GPGPU-Sim benefits for SST parallel simulation architecture
Notes: Description provided in ASC CSSE Milestone 6812.
Prior to this milestone, SST lacked the capability to model any external accelerator. We are now able to model a GPU accelerator in detail and analyze application and system behavior in fine detail.

## Slide 26
Backup Slides

## Slide 27: Thread Hierarchy Revisited
SIMT Core
Recall, kernel = grid of blocks of warps of threads
Threads are grouped into warps in hardware
Each block is dispatched to a SIMT core as a unit of work: All of its warps run in the core’s pipeline until they are all done.
Source: NVIDIA
Thread Block
(CTA)
32 Threads
32 Threads
32 Threads
Thread Block
(CTA)
32 Threads
32 Threads
32 Threads
Thread Block
(CTA)
32 Threads
32 Threads
32 Threads
Warps

## Slide 28: Inside a SIMT Core
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Done (Warp ID)
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 29: SIMT Stack
A: v = foo[tid.x];
B: if (v < 10)
C: v = 0;
else
D: v = 10;
E: w = bar[tid.x]+v;
Time
Handles Branch Divergence
D
E
0011
C
E
1100
B
-
1111
PC
RPC
Active Mask
E
-
1111
A
T1
T2
T3
T4
B
T1
T2
T3
T4
C
T1
T2
D
T3
T4
E
T1
T2
T3
T4
SIMT Stack
foo[] = {4,8,12,16};
One stack per warp

## Slide 30: Constant Cache
A Read-only cache for constant memory
GPGPU-Sim simulates 1 read ports
  A warp can access 1 constant cache locations in a single memory unit cycle
  If more than 1 locations accessed
    reads are serialized causing pipeline stalls
  # of ports is not configurable

## Slide 31: Coalescing
Combining memory accesses made by threads in a warp into fewer transactions
  E.g. if threads in a warp are accessing consecutive 4-byte sized locations in memory
    Send one 128–byte request to DRAM (coalescing)
    Instead of 32 4-byte requests
This reduces the number of transactions between SIMT cores and DRAM
  Less work for Interconnect, Memory Partition and DRAM

## Slide 32: Interconnection Network Model
Intersim (Booksim) a flit level simulator
  Topologies (Mesh, Torus, Butterfly, …)
  Routing (Dimension Order, Adaptive, etc. )
  Flow Control (Virtual Channels, Credits)
We simulate two separate networks
  From SIMT cores to memory partitions
    Read Requests, Write Requests
  From memory partitions to SIMT cores
    Read Replies, Write Acks

## Slide 33: PTX
Low-level data-parallel virtual ISA
  Instruction level
  Unlimited registers
  Parallel threads running in blocks; barrier synchronization instruction
Scalar ISA
  SIMT execution model
Intermediate representation in CUDA tool chain
.cu
.cl
NVCC
OpenCL Drv
PTX
ptxas
Fermi
Kepler
Maxwell
Pascal
Volta
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 34: SASS
Native ISA for Nvidia GPUs
  Better correlation with HW but less documented
  Related with Stream Multiprocessor(SM) version.
Scalar ISA
GPGPU-Sim use PTXPlus to represent both SASS and PTX
SASS mapped 1:1 into PTXPlus instruction
CUDA
Executable
cuobjdump
SASS
conversion
PTXPlus
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 35: PTX vs. SASS
SASS (PTXPlus)
l0x00000060:
add.half.u32 $r7, $r4, 0x00000400;
ld.global.u32 $r8, [$r4];
ld.global.u32 $r7, [$r7];
add.half.u32 $r0, $r5, $r0;
add.half.u32 $r6, $r8, $r6;
set.gt.u32.u32 $p0/$o127, s[0x0020], $r0;
add.half.u32 $r6, $r7, $r6;
add.half.u32 $r4, $r4, $r3;
@$p0.ne bra l0x00000060;
...
set.gt.u32.u32 $p0/$o127, $r2, const [0x0000];
@$p0.equ add.u32 $ofs2, $ofs1, 0x00000230;
@$p0.equ add.u32 $r6, s[$ofs2+0x0000], $r6;
@$p0.equ mov.u32 s[$ofs1+0x0030], $r6;
bar.sync 0x00000000;
PTX
$Lt_25_13570:
ld.global.s32 %r9, [%rd5+0];
add.s32 %r10, %r9, %r8;
ld.global.s32 %r11, [%rd5+1024];
add.s32 %r8, %r11, %r10;
add.u32 %r5, %r7, %r5;
add.u64 %rd5, %rd5, %rd6;
ld.param.u32 %r6, [size];
setp.lt.u32 %p2, %r5, %r6;
@%p2 bra $Lt_25_13570;
...
mov.u32 %r12, 127;
setp.gt.u32 %p3, %r3, %r12;
@%p3 bra $Lt_25_14082;
ld.shared.s32 %r13, [%rd10+512];
add.s32 %r8, %r13, %r8;
st.shared.s32 [%rd10+0], %r8;
$Lt_25_14082:
bar.sync 0;

## Slide 36: Interfacing GPGPU-Sim to applications
GPGPU-Sim compiles into a shared runtime library and implements the API:
  libcudart.so  CUDA runtime API
  libOpenCL.so  OpenCL API
Application
libcudart.so
CUDA runtime API
CUDA Driver
User level
Operating system
Hardware
GPU hardware
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 37: Interfacing GPGPU-Sim to applications
CUDA API layer
GPGPU-Sim compiles into a shared runtime library and implements the API:
  libcudart.so  CUDA runtime API
  libOpenCL.so  OpenCL API
Application
CUDA runtime API layer
CUDA runtime API
Functional model
Performance model
libcudart.so
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 38: GPGPU-Sim Runtime Flow
Notes: Impact statement from ASC CSSE Milestone 6812.
This is a stepping stone to achieve these goals; we still have some work to do. SST+GPU is the state-of-the-art in simulation capabilities. A literature review will reveal that, with this addition, SST provides more than other node-level simulation tool.
As we continue working on the GPU, memory, and interconnect models, we will get closer and closer to each of these impact statements.

## Slide 39
Slide Left Blank